## Slide 1
Assembling and Re-Assembling a PC
Parts, how they attach, and step-by-step procedure
Notes: Overview of building a desktop PC from parts, and taking it apart again.

## Slide 2
Before You Start: Tools & Safety
Tools
Phillips #2 screwdriver (magnetic)
Anti-static wrist strap
Cable ties, small bowl for screws
Thermal paste (if cooler has none)
Safety
Unplug the PSU and switch it off
Work on a hard, non-carpet surface
Touch bare metal case to discharge static
Hold boards by the edges; never force parts

## Slide 3
The 8 Main Parts
Case
Housing that holds and cools everything
Motherboard
Main board; connects all parts
CPU
The processor, brain of the PC
CPU Cooler
Removes heat from the CPU
RAM
Short-term working memory
SSD / HDD
Permanent storage for OS and files
Graphics Card
Renders video and games
Power Supply
Converts mains to PC voltages

## Slide 4
Step 1: Install the CPU
CPU
Attaches to: CPU socket on motherboard
Tools: None (hands only)
Place motherboard on its box, not on bare surfaces
Lift the socket retention lever
Match the gold triangle on CPU to the socket mark
Lower CPU flat, close the lever; never press hard
TIP Never touch the CPU pins or pads.
RE-ASSEMBLY / REMOVE: Lift lever, lift CPU straight up, store in its tray.
Notes: Step 1: Install the CPU. Place motherboard on its box, not on bare surfaces. Lift the socket retention lever. Match the gold triangle on CPU to the socket mark. Lower CPU flat, close the lever; never press hard.

## Slide 5
Step 2: Mount the CPU Cooler
CPU Cooler
Attaches to: On top of CPU, bolted to motherboard bracket
Tools: Screwdriver, thermal paste
Apply a pea-sized dot of paste on the CPU (skip if pre-applied)
Align cooler with the mounting holes
Tighten screws in a diagonal (X) pattern
Plug the fan cable into CPU_FAN header
TIP Remove any plastic film on the cooler base.
RE-ASSEMBLY / REMOVE: Unplug fan, loosen screws diagonally, twist gently, wipe old paste.
Notes: Step 2: Mount the CPU Cooler. Apply a pea-sized dot of paste on the CPU (skip if pre-applied). Align cooler with the mounting holes. Tighten screws in a diagonal (X) pattern. Plug the fan cable into CPU_FAN header.

## Slide 6
Step 3: Insert the RAM
RAM
Attaches to: DIMM slots on motherboard
Tools: None
Open the clips at both ends of the slot
Match the notch on RAM to the slot key
Use slots A2 and B2 for two sticks (see manual)
Press firmly on both ends until the clips click
TIP Dual channel gives better performance.
RE-ASSEMBLY / REMOVE: Push both clips outward and lift the stick straight out.
Notes: Step 3: Insert the RAM. Open the clips at both ends of the slot. Match the notch on RAM to the slot key. Use slots A2 and B2 for two sticks (see manual). Press firmly on both ends until the clips click.

## Slide 7
Step 4: Install the M.2 SSD
M.2 SSD
Attaches to: M.2 slot on motherboard
Tools: Small screwdriver
Remove the M.2 heatsink cover if present
Insert SSD at a 30 degree angle into the slot
Press down flat and fix with the small screw
Refit the heatsink cover
TIP Check the slot supports NVMe or SATA for your drive.
RE-ASSEMBLY / REMOVE: Remove the screw, the SSD pops up, pull it out.
Notes: Step 4: Install the M.2 SSD. Remove the M.2 heatsink cover if present. Insert SSD at a 30 degree angle into the slot. Press down flat and fix with the small screw. Refit the heatsink cover.

## Slide 8
Step 5: Fit the Power Supply
Power Supply
Attaches to: PSU bay at the rear of the case
Tools: Screwdriver, 4 screws
Place the PSU with its fan facing the vent
Align the four screw holes with the rear panel
Secure with four screws
Route the 24-pin, CPU and PCIe cables through the case
TIP Leave the PSU switch OFF while building.
RE-ASSEMBLY / REMOVE: Unplug all cables, unscrew four screws, slide out.
Notes: Step 5: Fit the Power Supply. Place the PSU with its fan facing the vent. Align the four screw holes with the rear panel. Secure with four screws. Route the 24-pin, CPU and PCIe cables through the case.

## Slide 9
Step 6: Mount Motherboard in Case
Motherboard in Case
Attaches to: Case standoffs and I/O shield
Tools: Screwdriver, 9 screws
Fit the I/O shield into the rear cutout
Check the standoffs match the board holes
Lower the board and align the rear ports
Fasten all screws, finger tight then snug
TIP Do not over-tighten; it can crack the board.
RE-ASSEMBLY / REMOVE: Unplug all cables, remove screws, lift board out.
Notes: Step 6: Mount Motherboard in Case. Fit the I/O shield into the rear cutout. Check the standoffs match the board holes. Lower the board and align the rear ports. Fasten all screws, finger tight then snug.

## Slide 10
Step 7: Install the Graphics Card
Graphics Card
Attaches to: PCIe x16 slot, rear bracket slots
Tools: Screwdriver
Remove the matching rear slot covers
Open the PCIe slot latch
Press the card in until the latch clicks
Screw the bracket and plug in PCIe power cables
TIP Use separate PCIe cables, not one daisy-chained.
RE-ASSEMBLY / REMOVE: Unplug power, unscrew, open latch, pull card out.
Notes: Step 7: Install the Graphics Card. Remove the matching rear slot covers. Open the PCIe slot latch. Press the card in until the latch clicks. Screw the bracket and plug in PCIe power cables.

## Slide 11
Step 8: Connect Storage & Cables
Storage & Cables
Attaches to: Drive bays, PSU, motherboard headers
Tools: Cable ties
Mount SATA drives in bays; connect SATA data and power
Plug in 24-pin ATX and 8-pin CPU power
Connect front USB, audio and fan cables
Tidy cables behind the tray with ties
TIP Good cable routing improves airflow.
RE-ASSEMBLY / REMOVE: Label cables, unplug in reverse, free the ties.
Notes: Step 8: Connect Storage & Cables. Mount SATA drives in bays; connect SATA data and power. Plug in 24-pin ATX and 8-pin CPU power. Connect front USB, audio and fan cables. Tidy cables behind the tray with ties.

## Slide 12
Step 9: Front Panel & First Boot
Front Panel & First Boot
Attaches to: Motherboard F_PANEL header, monitor, keyboard
Tools: Manual, monitor
Connect Power SW, Reset SW and LED pins per manual
Close the side panels, connect monitor to the GPU port
Switch on PSU, press power button
Enter BIOS, check parts, then install the OS
TIP No display? Reseat RAM and GPU first.
RE-ASSEMBLY / REMOVE: Power off, switch PSU off, unplug the mains cable.
Notes: Step 9: Front Panel & First Boot. Connect Power SW, Reset SW and LED pins per manual. Close the side panels, connect monitor to the GPU port. Switch on PSU, press power button. Enter BIOS, check parts, then install the OS.

## Slide 13
Re-Assembling: Take Apart in Reverse
1
Shut down, switch off PSU, unplug mains
2
Open side panels; photograph cable layout
3
Remove GPU, then drives and cables
4
Unplug motherboard cables and remove RAM
5
Unscrew and lift out the motherboard
6
Remove cooler, then CPU
7
Take out PSU; store parts in anti-static bags
To re-assemble, repeat Steps 1 to 9 in order.

## Slide 14
First Boot Troubleshooting
No power
Check PSU switch, 24-pin and 8-pin CPU cables, front panel Power SW pins
No display
Reseat RAM, plug monitor into GPU not motherboard, check PCIe power
Beeps or debug LEDs
Match the code to the motherboard manual: usually RAM, CPU or GPU
Overheating
Check cooler contact, fan header and case airflow direction