## Slide 1
Our Course
Course Full Details, explained topic by topic
HARDWARE · NETWORKING · CCNA · MCSA · LINUX

## Slide 2: Our Course:
✓ Hardware
✓ Networking
✓ CCNA Basic
✓ MCSA Basic
✓ Outlook
✓ MAC
✓ Linux
✓ Troubleshooting
✓ Q & A
****************Course Full Details *************

## Slide 3: Hardware:
Internal Part Of Computer
Mother Bord
Microprocessor
Memory
Storage ( HDD/SSD)
BIOS (Basic Input Output System)
Operating System
Windows Installation
Linux Installation
Windows Tools ( Control Panel)

## Slide 4: Hardware explained (1 of 5)
Internal Part Of Computer
The components inside the computer cabinet that work together to run programs.
Motherboard, CPU, RAM and storage
Power supply (SMPS) and cooling fans
Expansion cards: graphics, sound, network
Mother Bord
The main circuit board. Every other part plugs into it, and it lets them talk to each other.
CPU socket, RAM slots, expansion slots, ports
Chipset manages data flow between parts
Sizes (form factors): ATX, Micro ATX, ITX

## Slide 5: Hardware explained (2 of 5)
Microprocessor
The CPU, the brain of the computer. It fetches, decodes and executes instructions.
Speed is measured in GHz
Cores let it do several tasks at once
Main makers: Intel and AMD
Memory
RAM is the temporary working space that holds running programs and data for the CPU.
Volatile: data is lost when power is off
Types: DDR3, DDR4, DDR5
More RAM lets more programs run smoothly

## Slide 6: Hardware explained (3 of 5)
Storage ( HDD/SSD)
Permanent storage for the operating system, programs and files.
HDD: spinning magnetic disks, cheaper, slower
SSD: flash memory, no moving parts, much faster
Connect by SATA or NVMe (M.2)
BIOS (Basic Input Output System)
Firmware on the motherboard that runs first when the computer is switched on.
Runs POST to test the hardware
Finds the boot device and starts the OS
Boot order, date and time are set in BIOS setup

## Slide 7: Hardware explained (4 of 5)
Operating System
Software that manages the hardware and lets users and applications use the computer.
Manages memory, files, processes and devices
Provides the user interface
Examples: Windows, Linux, macOS
Windows Installation
Putting Windows on a computer from a bootable USB or DVD.
Set the boot device in BIOS and boot the installer
Create partitions and format the disk
Choose edition, create a user, install drivers

## Slide 8: Hardware explained (5 of 5)
Linux Installation
Installing a Linux distribution on a computer or virtual machine.
Write the ISO to a bootable USB
Choose language and partitions (/, swap, /home)
Create a user and install the boot loader (GRUB)
Windows Tools ( Control Panel)
Control Panel is the classic Windows place to change system settings.
Programs and Features: install or remove apps
Device Manager, Network and User Accounts
Newer Windows also has the Settings app

## Slide 9: Networking:
Networking Concept
Networking Media
Networking Device
Virus & Antivirus
Computer Address
Workgroup Vs Domain

## Slide 10: Networking explained (1 of 3)
Networking Concept
Connecting computers and devices so they can share data and resources.
Types: LAN, MAN and WAN
Topologies: bus, star, ring, mesh
Models: client-server and peer-to-peer
Networking Media
The path that carries signals between devices.
Copper: UTP cable (Cat5e, Cat6) with RJ-45
Fibre optic: light signals, long distance, high speed
Wireless: Wi-Fi and Bluetooth

## Slide 11: Networking explained (2 of 3)
Networking Device
Hardware that connects computers and controls how data moves.
Hub: repeats data to every port
Switch: forwards data by MAC address
Router: connects different networks by IP
Access point: provides Wi-Fi
Virus & Antivirus
A virus is harmful code that spreads and damages data. Antivirus finds and removes it.
Types: virus, worm, trojan, ransomware, spyware
Spreads by email attachments, USB drives, downloads
Antivirus scans and needs regular updates

## Slide 12: Networking explained (3 of 3)
Computer Address
Identifiers that locate a computer on a network.
IP address: logical, e.g. 192.168.1.10 (IPv4)
MAC address: physical, 48-bit, fixed in the NIC
Hostname: friendly name resolved by DNS
Workgroup Vs Domain
Two ways to organise computers in a network.
Workgroup: peer-to-peer, each PC has its own accounts, small networks
Domain: a server (Active Directory) manages users and policies centrally
Domain scales to hundreds of computers

## Slide 13: CCNA Basic:
OSI Model
Protocol (Routed)
Protocol (Routing)
✓ RIP
✓ OSPF
✓ EIGRP
NAT Network Address Translation
VLAN (virtual local area network)
ACL (Access Control list )
WLC ( wireless LAN controller)

## Slide 14: CCNA Basic explained (1 of 4)
OSI Model
A 7-layer reference model that describes how data travels across a network.
Application, Presentation, Session, Transport, Network, Data Link, Physical
Each layer has one job
Helps troubleshoot layer by layer
Protocol (Routed)
Protocols that carry user data and can be forwarded from network to network.
Example: IP (IPv4 and IPv6)
Packets carry source and destination addresses
Routers forward them by destination network

## Slide 15: Protocol (Routing): RIP, OSPF, EIGRP
Routing protocols let routers learn about networks and choose the best path to each.
RIP
Routing Information Protocol. Distance-vector.
Metric: hop count
Maximum 15 hops
Simple, slow to converge, small networks
OSPF
Open Shortest Path First. Link-state.
Open standard, many vendors
Metric: cost, built on areas
Fast convergence, large networks
EIGRP
Enhanced Interior Gateway Routing Protocol.
Cisco advanced distance-vector (hybrid)
Metric uses bandwidth and delay
Fast convergence, easy to configure

## Slide 16: CCNA Basic explained (3 of 4)
NAT Network Address Translation
Translates private IP addresses to a public address so many devices share one Internet connection.
Static NAT, Dynamic NAT and PAT (overload)
Hides internal addresses
Configured on a router or firewall
VLAN (virtual local area network)
Splits one physical switch into separate logical networks.
Each VLAN is its own broadcast domain
Less broadcast traffic and better security
Inter-VLAN routing links VLANs; trunk ports carry many VLANs

## Slide 17: CCNA Basic explained (4 of 4)
ACL (Access Control list )
A list of permit or deny rules that filters traffic on a router or switch.
Checked top to bottom, first match wins
Standard (source) and Extended (source, destination, port)
Implicit deny at the end
WLC ( wireless LAN controller)
A central device that manages many wireless access points.
Controls SSIDs, security and AP settings
Handles roaming between access points
Manages lightweight APs through CAPWAP

## Slide 18: Firewall Basic:
What is Firewall?
How it Work Firewall?
How to Install Palo Alto Firewall In VMware
Configuration Palo Alto Firewall

## Slide 19: Firewall Basic explained (1 of 2)
What is Firewall?
A security device or software that controls traffic between a trusted network and an untrusted one such as the Internet.
Can be hardware or software
Allows or blocks traffic by rules
Examples: Palo Alto, Cisco ASA, Windows Firewall
How it Work Firewall?
It inspects each packet or session and compares it with its rule list.
Packet filtering: IP address, port, protocol
Stateful inspection tracks connections
Next-generation firewalls also see applications and users

## Slide 20: Firewall Basic explained (2 of 2)
How to Install Palo Alto Firewall In VMware
Run the Palo Alto VM-Series firewall as a virtual machine to practise.
Import the image into VMware
Add network adapters for management and data
Power on, log in on the console, set the management IP
Configuration Palo Alto Firewall
Setting up the firewall so it passes and blocks the right traffic.
Configure interfaces and security zones
Create security policies and NAT rules
Commit the changes to apply them

## Slide 21: MCSA Basic:
Active Directory
Domain Controller
✓ ADC , RODC , CDC ,Root DC
FSMO Role
DHCP
DNS
Remote Desktop / Access
Group Policy
MMC
WDS
File Service
✓ FSRM
✓ DFS

## Slide 22: MCSA Basic explained (1 of 6)
Active Directory
Microsoft directory service that stores users, computers and groups and controls access in a domain.
One login for the whole domain
Structure: forest, domain, OU
Runs on Windows Server (AD DS)
FSMO Role
Flexible Single Master Operations: five special roles held by domain controllers.
Forest: Schema Master, Domain Naming Master
Domain: RID Master, PDC Emulator, Infrastructure Master
Each role is held by one DC at a time

## Slide 23: Domain Controller: ADC, RODC, CDC, Root DC
ADC
Additional Domain Controller. An extra DC in the same domain for backup and load sharing.
RODC
Read-Only Domain Controller. Keeps a read-only copy, used in branch offices with weaker security.
CDC
Child Domain Controller. A DC of a child domain placed under a parent domain.
Root DC
The first domain controller of the forest root domain.

## Slide 24: MCSA Basic explained (3 of 6)
DHCP
Dynamic Host Configuration Protocol gives IP settings to devices automatically.
Leases IP address, mask, gateway and DNS
DORA: Discover, Offer, Request, Acknowledge
Scope sets the range; reservations fix addresses
DNS
Domain Name System translates names into IP addresses.
Forward lookup: name to IP
Reverse lookup: IP to name
Active Directory depends on DNS

## Slide 25: MCSA Basic explained (4 of 6)
Remote Desktop / Access
Connect to and control another computer or server over the network.
RDP uses TCP port 3389
Enable Remote Desktop and allow users
Remote Access can also mean VPN into the network
Group Policy
Central rules applied to users and computers in a domain.
GPOs link to a site, domain or OU
Examples: password rules, drive mapping, restrictions
gpupdate refreshes policies

## Slide 26: MCSA Basic explained (5 of 6)
MMC
Microsoft Management Console. A window that hosts management tools called snap-ins.
Open it by typing mmc
Add snap-ins such as Computer Management
Save the console as an .msc file
WDS
Windows Deployment Services installs Windows on many computers over the network.
Clients boot using PXE
Serves boot and install images
Works with DHCP and Active Directory

## Slide 27: File Service: FSRM and DFS
File Service is the Windows Server role for sharing and managing files and folders.
FSRM
File Server Resource Manager. Controls what is stored on file servers.
Quotas limit folder size
File screening blocks file types
Storage reports show usage
DFS
Distributed File System. Makes shared folders easier to reach and safer.
Namespace joins many shares into one path
Replication keeps copies in sync
Users do not need to know the server name

## Slide 28: Virtualization technology / Outlook
Virtualization technology:
What is VMware?
Introduction virtualization
Outlook:
Outlook Configuration
Outlook Troubleshooting

## Slide 29: Virtualization technology explained
What is VMware?
A company and software family for virtualization.
Workstation runs virtual machines on a PC
ESXi and vSphere run them on servers
Each virtual machine has its own operating system
Introduction virtualization
Running several virtual machines on one physical computer.
A hypervisor shares CPU, RAM and storage
Saves hardware, power and cost
Snapshots make backup and testing easy

## Slide 30: Outlook explained
Outlook Configuration
Setting up an email account in Outlook.
Needs email address, password and server type
IMAP or POP3 for incoming, SMTP for outgoing
Microsoft 365 and Exchange often set up automatically
Outlook Troubleshooting
Fixing common mail problems.
Cannot send or receive: check internet, password and server settings
Will not start: use safe mode or create a new profile
Repair damaged PST files with the Inbox Repair tool

## Slide 31: MAC / Linux
MAC :
Introduction to MAC (iOS)
How to Install MAC (iOS)
Basic Configuration
Linux:
Introduction to Linux Operating System
How to install Linux iOS
Basic Configuration

## Slide 32: MAC explained
Introduction to MAC (iOS)
Mac is Apple's computer line. Its operating system is macOS.
Built on Unix
Finder, Dock and Spotlight
Apps come from the App Store
How to Install MAC (iOS)
Installing or reinstalling the Mac system.
Start in macOS Recovery (Command + R)
Use Disk Utility to erase the disk
Choose Reinstall macOS, internet needed
Basic Configuration
First settings after install.
Create a user, sign in with Apple ID
Connect to Wi-Fi in System Settings
Run Software Update, set up Time Machine

## Slide 33: Linux explained
Introduction to Linux Operating System
A free, open-source operating system built on the Linux kernel.
Used on servers, desktops and cloud
Distributions: Ubuntu, Red Hat, Debian
Terminal and graphical desktop
How to install Linux iOS
Installing a Linux distribution (Linux, not iOS).
Download the ISO, make a bootable USB
Boot it and choose Install
Partition the disk, create a user, install GRUB
Basic Configuration
First settings after install.
Set hostname and network (IP, DNS)
Manage users and permissions
Update packages with apt or dnf

## Slide 34: Troubleshooting
Troubleshooting
Finding the cause of a problem and fixing it step by step.
Identify the problem and what changed
Think of the most likely cause and test it
Fix it, confirm it works, write it down
Where it is used in this course
The same method applies to every module above.
Hardware: no power, no display, beeps
Network: no IP, cannot reach the server
Outlook and operating systems: errors and slow start

## Slide 35
Q & A
Questions and discussion