## Slide 1
ROM, CMOS and BIOS
What they are, how they differ, and how BIOS starts your PC
BIOS
CMOS

## Slide 2
Big Picture: Where They Live
CPU
RAM
BIOS chip
CMOS
battery
I/O
ROM
Type of permanent memory. The BIOS program is stored in a ROM/flash chip.
BIOS
Firmware program that starts the hardware and loads the OS.
CMOS
Tiny battery-backed memory that remembers BIOS settings and the clock.

## Slide 3
What is ROM?
ROM = Read-Only Memory
Non-volatile: data stays when power is off
Holds permanent instructions such as firmware
Written by the manufacturer; rarely changed
Fast and reliable; stores boot code
Types of ROM
PROM
Programmed once by user
EPROM
Erased with UV light, reprogrammed
EEPROM
Erased electrically, byte by byte
Flash
Block-erasable; used for modern BIOS

## Slide 4
What is CMOS?
Two meanings: a chip technology, and the small memory on the motherboard
Full form: Complementary Metal-Oxide-Semiconductor
CMOS memory stores BIOS settings: date, time, boot order, hardware options
Needs constant power: a CR2032 3V coin cell battery keeps it alive
Also runs the Real-Time Clock (RTC)
Dead battery = time resets and settings lost
CR2032
3V
Coin cell battery
Lasts about 3 to 5 years

## Slide 5
ROM vs CMOS
Feature | ROM | CMOS
Full form | Read-Only Memory | Complementary Metal-Oxide-Semiconductor
Purpose | Stores permanent firmware | Stores settings and the clock
Contents | BIOS program code | Date, time, boot order, config
Volatility | Non-volatile | Volatile, kept alive by battery
Power needed | None to keep data | CR2032 coin cell battery
Changeable? | Rarely (flash update) | Yes, via BIOS Setup
Typical size | Several MB | A few hundred bytes to KB
If it fails | PC cannot boot | Time resets, settings lost

## Slide 6
BIOS vs CMOS: Program vs Settings
BIOS
Firmware program
Stored in flash ROM
Runs POST and boot
Updated by flashing
CMOS
Small settings memory
Battery-backed RAM
Holds boot order, time
Changed in BIOS Setup
reads / writes
Analogy: BIOS is the instruction manual built into the PC. CMOS is the sticky note of your personal preferences that the manual reads every startup.

## Slide 7
What is BIOS?
BIOS = Basic Input/Output System
Firmware stored on a chip on the motherboard (flash ROM)
The first code the CPU runs when power is switched on
Acts as a bridge between hardware and the operating system
Introduced by IBM PCs in 1981; now mostly replaced by UEFI
Provides the BIOS Setup utility to change settings
Operating System
BIOS (firmware)
Hardware: CPU, RAM, disks
Layers of a PC

## Slide 8
Four Main Functions of BIOS
1
POST
Power-On Self Test checks CPU, RAM, keyboard and video before booting.
2
Bootstrap loader
Finds a bootable drive and loads the boot sector to start the OS.
3
BIOS drivers
Basic low-level routines to talk to keyboard, disks and display.
4
BIOS Setup
Menu to change boot order, date, time and hardware options.

## Slide 9
Boot Process: Step by Step
1. Power on
PSU powers the board
2. Reset vector
CPU jumps to BIOS code
3. POST
Tests CPU, RAM, GPU
4. Init hardware
Sets up devices
5. Read CMOS
Loads saved settings
6. Find boot device
Checks boot order
7. Boot loader
Loads from drive
8. OS starts
Windows / Linux loads
CMOS is read at step 5, so wrong settings or a dead battery can change how the PC starts.

## Slide 10
Legacy BIOS vs UEFI
Feature | Legacy BIOS | UEFI
Era | 1980s to about 2010 | Modern PCs (2010+)
Interface | Text menus, keyboard only | Graphical, mouse support
Disk support | MBR, up to 2 TB | GPT, over 2 TB
Boot speed | Slower | Faster, Fast Boot
Security | None built in | Secure Boot
Mode | 16-bit | 32-bit / 64-bit
Storage | Small flash ROM | Larger flash (16 MB+)

## Slide 11
Using BIOS Setup & Resetting CMOS
Enter BIOS Setup
Restart and press Del, F2, F10, F12 or Esc at the logo
Key varies by maker (see the manual)
Common settings: boot order, date/time, XMP/RAM speed, virtualization, Secure Boot
Reset (Clear) CMOS
Shut down and unplug the power
Remove the CR2032 battery for 1 to 5 minutes (or use the CLR_CMOS jumper)
Reinsert the battery or restore the jumper
Power on and set the date/time again
CAUTION Never turn the PC off while updating (flashing) the BIOS. A failed flash can make the board unbootable.

## Slide 12
Key Takeaways
ROM
Permanent memory that stores firmware.
BIOS
The firmware program that tests hardware and boots the OS.
CMOS
Battery-backed memory for settings and the clock.
UEFI
The modern replacement for legacy BIOS.