## Slide 1
Network Topology
How computers and devices are arranged and connected: bus, ring, star, tree, hybrid and mesh
Notes: Overview of the six network topologies, with how each works and its pros and cons.

## Slide 2
What is topology?
Topology is the way the devices in a network are arranged and connected to each other.
Physical topology
The real layout of cables and devices.
Logical topology
How data actually flows between devices.
Six types of topology
1
Bus
2
Ring
3
Star
4
Tree
5
Hybrid
6
Mesh

## Slide 3
Bus topology: how data travels
Terminator
Ground
Coaxial cable
BNC T connector
PC1
Sender
PC2
Detect & discard
PC3
Receive & reply
PC4
Detect & discard
PC1 sends data to PC3. The signal travels along the whole cable, every PC hears it, PC2 and PC4 discard it, and PC3 accepts it and replies. The terminator stops the signal bouncing back.
Notes: Bus: one shared cable. All PCs see every signal; only the addressed PC keeps it.

## Slide 4
Bus topology: parts, pros and cons
1
Coaxial cable
The shared backbone
2
BNC T connector
Attaches each PC to the cable
3
Terminator
Absorbs the signal at the cable end
4
Ground
Safely earths the cable
All devices share one main cable. Each PC attaches with a BNC T connector, and both ends of the cable are closed off.
Pros
Cheap, uses little cable
Simple to set up
Cons
One cable break stops all
Slower as PCs are added

## Slide 5
Ring topology
Flow of
message
Computer A
Computer B
Computer C
Computer D
↻
Each computer connects to exactly two neighbours, forming a closed loop. Messages travel around the ring in one direction. A dual ring adds a second ring as backup.
Pros
Orderly, predictable data flow
Dual ring survives one break
Cons
Single ring: one break can stop it
Hard to add or remove nodes

## Slide 6
Star topology
Computer
Computer
Computer
Computer
Printer
Hub / Switch
All devices connect to a central hub or switch. Cable: UTP (Unshielded Twisted Pair) with RJ45 connectors. A hub repeats data to every port; a switch sends it only to the right port.
Pros
Easy to add or remove PCs
A cable fault hits only one PC
Cons
Hub/switch failure stops all
Needs more cable

## Slide 7
Tree topology
Backbone / Server
S1
A
B
S2
C
D
S3
E
F
Nodes
A hierarchy of star networks joined by a backbone cable. Switches (S1, S2, S3) each serve a group of nodes, and a server sits on the backbone. Think of it as levels, like a tree.
Pros
Scales to many nodes
Faults stay inside one branch
Cons
Backbone failure splits network
Needs a lot of cabling

## Slide 8
Hybrid topology
Ring network
Star network
Bus network
Hybrid network
A mix of two or more topologies joined together, here a ring, a star and a bus. Used in large networks such as ATM and bank networks.
Pros
Flexible and scalable
Combines the strengths of each
Cons
Complex to design
Costly to build

## Slide 9
Mesh topology
PC
PC
PC
PC
PC
Every host is directly connected to every other host. With n hosts you need n(n-1)/2 links: 5 hosts need 10. Used in mission-critical networks like airports and bank ATMs.
Pros
Very reliable, many paths
No single point of failure
Cons
Many cables and ports
Most costly to build

## Slide 10
Comparing the topologies
Topology | Connected through | Main weakness
Bus | One shared cable | Cable break stops everyone
Ring | A closed loop | One break can stop a single ring
Star | Central hub or switch | Central device is a single point of failure
Tree | Stars joined by a backbone | Backbone failure splits the network
Hybrid | Mix of topologies | Complex and costly
Mesh | Every host linked to every other | Most cables, highest cost

## Slide 11
Key takeaways
1
Topology The arrangement of devices in a network
2
Bus & Ring Cheap and simple, but a break can hurt
3
Star & Tree Most common, easy to manage
4
Hybrid & Mesh Flexible or highly reliable, but costly