## Slide 1
Networking Media
Wired, wireless, connectors, cabling standards and tools: a complete guide
Coax
UTP
Fiber
RF

## Slide 2: What is networking media?
The physical or wireless path that carries data signals between devices on a network.
Carries signals
Electrical pulses (copper), light (fiber) or radio waves (wireless) represent the bits 0 and 1.
Sets the limits
Media decides bandwidth, maximum distance, immunity to noise and cost.
Two families
Guided (bounded) media use a physical cable. Unguided (unbounded) media use open air.
Notes: Networking media is the channel between sender and receiver.

## Slide 3: Classification of communication media
Communication media
Wired: guided / bounded
Coaxial: Cable TV
Twisted pair: LAN, Metro Ethernet
Optical fiber: CAN, MAN, WAN
Wireless: unguided / unbounded
Radio waves (2.4 and 5 GHz): Wi-Fi
Microwave: SATCOM, VSAT
Infrared: remote controls

## Slide 4: Coaxial cable
1
Outer jacket: Protective PVC sheath
2
Braided shield: Copper braid blocks interference
3
Foil shield: Extra layer, higher frequency protection
4
Dielectric: Insulator that keeps the center centred
5
Inner conductor: Solid copper core carrying the signal
Speed and distance
Classic Ethernet (10BASE5): 10 Mbps up to 500 m. 10BASE2: 185 m.
Uses and connectors
Cable TV, CCTV, broadband (DOCSIS). BNC and F-type connectors.

## Slide 5: Twisted pair cable
Pairs of copper wires are twisted together so that interference from each wire cancels out. A cable holds 4 pairs (8 wires). Maximum run: 100 m.
STP: Shielded
Foil or braid shield around pairs.
Better noise immunity.
Used in industrial networks and R&D labs.
Costlier, needs grounding.
UTP: Unshielded
No shield; relies on the twists.
Cheap, thin, easy to install.
Used in general networks, i.e. LAN, offices, homes.

## Slide 6: Twisted pair categories
Category | Max speed | Bandwidth | Typical use
Cat5 | 100 Mbps | 100 MHz | Older Fast Ethernet
Cat5e | 1 Gbps | 100 MHz | Fast and Gigabit Ethernet
Cat6 | 10 Gbps (up to 55 m) | 250 MHz | High-speed, short distances
Cat6a | 10 Gbps (100 m) | 500 MHz | 10 Gigabit Ethernet, longer runs
Cat7 / Cat8 | 10 / 25-40 Gbps | 600 / 2000 MHz | Data centres (shielded)
All twisted pair categories are limited to 100 m per segment (Cat8: 30 m).

## Slide 7: Fiber optic cable
Sends data as pulses of light through glass strands: highest speed, longest distance, immune to electrical interference.
 | Single-mode (SMF) | Multi-mode (MMF)
Core | About 9 µm | 50 or 62.5 µm
Light source | Laser | LED / VCSEL
Distance | Up to 10-100+ km | Up to 300-550 m at 10G
Use | WAN, MAN, backbone | CAN, data centres, buildings
Speed
Commonly 10 to 400 Gbps per link, and far higher in labs. Not 300 Mbps.
Notes: Correction to class slide: fiber is not limited to 300 Mbps. That figure belongs to slower wireless technologies; fiber reaches 100 Gbps and beyond.

## Slide 8: UTP cable types
Cable | Connects | Examples
Straight-through | Different devices | PC to switch, router to switch
Crossover | Same devices | Switch to switch, PC to PC
Rollover (console) | Admin to device console port | PC to switch or router console
Modern NICs and switches support Auto-MDI/MDIX, so a straight-through cable usually works for both cases. Exams still ask the classic rule.

## Slide 9: T568A vs T568B wiring
Pin | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
T568B | W-Orange | Orange | W-Green | Blue | W-Blue | Green | W-Brown | Brown
T568A | W-Green | Green | W-Orange | Blue | W-Blue | Orange | W-Brown | Brown
Straight-through
T568B on both ends (or A on both). Pin 1 to 1, 2 to 2, and so on.
Crossover
T568A on one end, T568B on the other. Pairs 2 and 3 swap.

## Slide 10: Pin function: TX and RX
Pin | PC (NIC) end | Hub/Switch end | Crossover result
1 | TX+ | RX+ | Pin 1 meets pin 3
2 | TX- | RX- | Pin 2 meets pin 6
3 | RX+ | TX+ | Pin 3 meets pin 1
6 | RX- | TX- | Pin 6 meets pin 2
4, 5, 7, 8 | Unused in 10/100 Mbps | Unused | Straight (used in Gigabit)
A transmitter must always connect to a receiver. Same devices both transmit on 1 and 2, so the cable must swap the pairs.

## Slide 11: Wireless media
Radio waves
2.4 and 5 GHz
Wi-Fi, Bluetooth, passes through walls
Microwave
1 to 300 GHz
SATCOM, VSAT, line of sight, long distance
Infrared
Above microwave
Remote controls, short range, no walls
Easy to deploy and mobile, but prone to interference, eavesdropping and signal loss.

## Slide 12: Connectors
Connector | Pins / type | Used with
RJ-45 | 8 pins | Ethernet twisted pair
RJ-11 | 6 position (2 to 4 wires) | Telephone, DSL
DB9 (male / female) | 9 pins | Serial and console (RS-232)
BNC | Twist-lock coaxial | Coax, CCTV, 10BASE2
V.35, X.21, EIA-530 | Large serial | Router to modem or CSU/DSU

## Slide 13: Cabling tools
Crimping tool
Presses the RJ-45 plug onto the wires. Most also strip and cut cable.
Cable tester
Master and remote units. LEDs light pins 1 to 8 in order, showing opens, shorts or crossed wires.
Also needed
RJ-45 plugs, cable stripper, punch-down tool for patch panels.

## Slide 14: Making a cable: steps
1
Strip about 2.5 cm of jacket
2
Untwist and arrange pairs in T568B or T568A order
3
Flatten and trim wires evenly
4
Insert into RJ-45, clip facing away, pin 1 on the left
5
Crimp, repeat on the other end, test

## Slide 15: Media comparison
Medium | Speed | Distance | Cost | EMI immunity
Coaxial | 10 Mbps to Gbps | 185-500 m | Medium | Good
UTP | 10 Mbps to 40 Gbps | 100 m | Low | Poor
STP | Same as UTP | 100 m | Medium | Good
Fiber | 10 to 400+ Gbps | Up to 100+ km | High | Immune
Wireless | Mbps to Gbps | Short to global | Low to high | Poor

## Slide 16
Key takeaways
Guided media: coax, twisted pair, fiber. Unguided: radio, microwave, infrared.
UTP for LANs, fiber for backbones and distance, wireless for mobility.
Straight-through for different devices, crossover for same, rollover for console.
Crossover = T568A on one end and T568B on the other.
Always test the cable after crimping.